FAIR Cryogenic Nomenclature System

| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

Digit 1, 2, 3, 4 	Accelerator systems

Digit 5 = Y		FAIR Cryogenics

Digit 6 = 		Cryogenic devices

D		Distribution box;

T		Transfer line;

C	interConnection between transfer line sections, feedboxes and distribution box;

F		Feedbox;

J	Jumper connection between feedbox and magnet cryostat;

B		Vaccum Barrier;

R		Return box (endbox);

W		Warm piping for Cryogenics;

Cryogenic Devices

YD      Cryogenic Distribution box

YT      Cryogenic Transfer line;

YC      Cryogenic interConnection between transfer line sections, feedboxes and distribution box;

YF      Cryogenic Feedbox;

YJ       Cryogenic Jumper connection between feedbox and magnet cryostat;

YR      Cryogenic Return box (endbox);

YW     Warm piping for Cryogenics.

Digit 7 = 	Subsystem in cryogenic devices

I			Instrumentations;

H			Headers (cryogenic piping);

V			Valves;

X			helium heat eXchanger in subcooler;

S			thermal Shield;

If Digit 7 = I, then

8 = T		Temperature sensor;

8 = P		Pressure sensor;

9 = A	Absolute pressure sensor;

9 = B	Barometric pressure sensor;

9 = D	Differential pressure sensor;

9 = R	Gauge pressure sensor;

9 = V	Vacuum pressure sensor;

8 = F		Flow meter;

8 = L		Level meter;

9 = H	liquid Helium meter;

9 = N	liquid Nitrogen meter;

For example,

- - - - Y F I P B

for

one Barometric Pressure Sensor in one Cryogenic Feedbox

If Digit 7 = H, then

Digit 8 =

1	Helium low temperature supercritical/liquid supply line;

2	Helium low temperature return line;

3	Helium shield temperature supply line;

4	Helium shield temperature return line;

5	Helium ambient temperature supply line;

6	Helium ambient temperature return line;

7	Helium purge line;

8	Helium low/ambient temperature multipurpose line;

If Digit 7 = V, then

Digit 8 =

C		Control valve;

E		Electric valve;

P		Pneumatic valve;

Q		Quench valve;

S		Safety valve;

N		Non-return valve (check valve);

H		Hand valve;

O		On/off valve (digital valve);

AND

Digit 9 =

1	Helium low temperature supercritical/liquid supply line;

2	Helium low temperature return line;

3	Helium shield temperature supply line;

4	Helium shield temperature return line;

5	Helium ambient temperature supply line;

6	Helium ambient temperature return line;

7	Helium purge line;

8	Helium low/ambient temperature multipurpose line;

Examples,

- - - - Y D V C 1

for

one Control Valve on the helium low temperature supercritical/liquid supply line in one Cryogenic Distribution box