LSA Basics for Developers
Training Course
J.Fitzek
01.02.2018

---
Agenda
- LSA System, LSA @ GSI
- Concepts in LSA
  - Accelerators and Layout, Parameter Hierarchy
  - Contexts
  - Settings
  - Trim
- LSA API and Examples

---
Agenda
- LSA System, LSA @ GSI
- Concepts in LSA
  - Accelerators and Layout, Parameter Hierarchy
  - Contexts
  - Settings
  - Trim
- LSA API and Examples

---
What is LSA? 1/2
- The LSA Project started at CERN in 2001
- LSA was originally called “LHC software architecture”,
  but is now being used widely at CERN
- Core component of the CERN control system at operating level
- Central part for settings management
- Highly data driven, DB is the master and contains all needed information about optics, devices, contexts, etc
- ONE database schema for all accelerators

---
What is LSA? 2/2
- Parameters are organized in hierarchies
  (from physics to hardware)
- Consistent settings generation and management for all levels
- Devices are accessed using an abstraction layer called JAPC
  that hides middleware specifics
- With LSA, machines are operated on physics level in a consistent way
- Generic approach that allows to just “model” an accelerator within the LSA system and then manage settings for it

---
LSA Architecture Overview
Client
Applications
RMI
LSA Server
LSA Service API
LSA CORE
(Settings, Trim, Generation, Optics)
Data Access Objects
JAPC
Spring JDBC
JAPC Plugins
ZeroMQ
JDBC
LSA DB
Devices

---
LSA Runtime Setup: 2-tier or 3-tier
- 3-tier Setup: Standard setup for clients, e.g. application development
- 2-tier Setup (for LSA core development)
LSA DB
Proxy
lsa-service
lsa-core
Client
Server
DB
LSA DB
lsa-service
lsa-core
DB
Client
Applications
Applications

---
LSA @ GSI
- Project Team at GSI “FAIR Datenversorgung” started end of 2008 (project leader: David Ondreka)
  with members from SYS, ACO, OPE, Machine experts
- Goal is an integrated, homogeneous data supply and settings management for all FAIR accelerators
- As software component for settings management the CERN framework LSA was evaluated and chosen for GSI
- LSA is being enhanced by CERN and GSI in a collaboration since 2008
  => LSA will be the central component for settings management within the new FAIR control system

---
Agenda
- LSA System, LSA @ GSI
- Concepts in LSA
  - Accelerators and Layout, Parameter Hierarchy
  - Contexts
  - Settings
  - Trim
- LSA API and Examples

---
LSA Concepts: Accelerator
GSI_HEBT
FAIR_HEBT

---
LSA Concepts: Particle Transfer, AcceleratorZone
- Particle Transfers are parts of the
  accelerator with same optics and
  same timing, typically defined
  between junction points
- Particle Transfers can be divided
  into several Accelerator Zones,
  if beam attributes (charge..) change,
  otherwise it is 1:1
- Particle Transfers are grouped into
  Transfer Lines, e.g. for optics calculation

---
LSA Concepts: Particle Transfer, AcceleratorZone
- Particle Transfers are parts of the
  accelerator with same optics and
  same timing, typically defined
  between junction points
- Particle Transfers can be divided
  into several Accelerator Zones,
  if beam attributes (charge..) change,
  otherwise it is 1:1
- Particle Transfers are grouped into
  Transfer Lines, e.g. for optics calculation
Particle Transfer
Accelerator Zone
Transfer Line

---
LSA Concepts: Device
- Devices are assigned to Accelerator Zones
- Devices in LSA are imported either from FESA or from DeviceAccess
- Devices have a DeviceType, e.g. BasicPS (for “Basic Power Supply”) together with the Properties defined in FESA
Controls DB
Accelerators
Particle Transfers
Accelerator Zones
CDB Infos
  (e.g. Calibration Curves, min/max,..)
Devices
Device Types
 (Type, Properties, Fields)
DevAcc DB
LSA DB
FESA DB

---
LSA Concepts: Parameter Hierarchy
- A parameter defines a settable or measurable entity of the system
- It represents a property of a given device:
  the device can be physical such as a specific power converter,
  logical such as the SIS100 Beam or grouping of equipment
- Parameters are described in a hierarchy
  - represents the logical structure from high-level physics parameters, like beam energy, to machine parameters, like current for a power converter
  - “Roots” are usually changed by operators and are physics parameters
  - “Leaves” are usually hardware parameters
  - Only the lowest parameter level is send to the hardware
  - Settings are kept for all levels

---
Agenda
- LSA System, LSA @ GSI
- Concepts in LSA
  - Accelerators and Layout, Parameter Hierarchy
  - Contexts
  - Settings
  - Trim
- LSA API and Examples

---
FAIR Operation Scenarios
Examples for periodic Patterns, each dominated by one main experiment
Unilac
p-Linac
SIS18
SIS100
CR
HESR
pbar + RIB ext. target (U28+) + AP (HE)
Unilac
SIS18
SIS100
CBM + RIB ext. target (U73+) + AP (LE)
Unilac
SIS18
SIS100
ESR
RIB ext. target (U28+) + ESR

---
LSA Concepts: Context (Patterns, Chains)
Beam Production Chain (BPC)
Organisational structure to manage
parallel operation and beam transfer
through the FAIR accelerator facility
Defines sequence and parameters of
beam lines from the ion-source
up to an experiment
Pattern
Grouping of Beam Production Chains
that are executed periodically
=> For 2018
One BPC per Pattern
Multiple Patterns in Round Robin
Similar to working with Virtual Accelerators
Chains
SIS18
SIS100
HESR
SIS18
SIS100
HESR
Pattern
SIS18
SIS100
HESR
Chains
SIS18
SIS100
HESR
SIS18
SIS100
HESR
Pattern
SIS18
SIS100
HESR
Chains
SIS18
SIS100
HESR
SIS18
SIS100
HESR
Pattern
SIS18
SIS100
HESR

---
LSA Contexts: Pattern Group
- Several Patterns can be resident in the machine
- Disjoint Patterns can be active at the same time! (e.g. Cryring and SIS18)
- Patterns are therefore organized in Pattern Groups, that contain
  patterns for different areas of the accelerator complex

---
LSA Contexts: Pattern Group
- Several Patterns can be resident in the machine
- Disjoint Patterns can be active at the same time! (e.g. Cryring and SIS18)
- Patterns are therefore organized in Pattern Groups, that contain
  patterns for different areas of the accelerator complex
Pattern Group 1
Pattern Group 2

---
LSA Concepts: Context (Beam Processes 1/2)
- Beam Production Chains are composed of Beam Processes
- Beam Processes describe physics processes
  that are going on in the machine (e.g. injection, ramp, extraction)
- Beam Processes are defined per Particle Transfer
- Settings are kept per Beam Process
- Beam Processes are categorized in BEAM_IN and BEAM_OUT

---
Agenda
- LSA System, LSA @ GSI
- Concepts in LSA
  - Accelerators and Layout, Parameter Hierarchy
  - Contexts
  - Settings
  - Trim
- LSA API and Examples

---
LSA Concept: Setting 1/2
- context in LSA represents something, that can be executed in the machine: BeamProcess, BeamProductionChain, Pattern
- setting is a scalar/function for a parameter depending on a context
- settings are stored for ALL levels of the parameter hierarchy
Parameter
Setting
Context (Beam Process)

---
LSA Concept: Setting 2/2
- a setting consists of target and correction value
- target values are calculated using the accelerator model
- also top level operator input is configured to be placed in target
- => most of the time, target is used only, and if necessary,
  a separate correction-parameter exists
- => correction values are applied only, if the model seems incorrect
  (expert use, e.g. during commissioning, machine development)
Setting
1.0
0.2
1.2
 =>
Target + Correction = Value

---
Agenda
- LSA System, LSA @ GSI
- Concepts in LSA
  - Accelerators and Layout, Parameter Hierarchy
  - Contexts
  - Settings
  - Trim
- LSA API and Examples

---
What is a trim?
- A trim is a coherent modification of settings,
  plus propagation of changes down the parameter hierarchy
- All applied trims are archived and can be reverted
- The changed settings are also sent to the hardware,
  if the context is resident
- The Trim calculation is based on three main concepts:
  - Makerule
  - Linkrule
  - Incorporation Rule

---
LSA Trim: Makerule 1/2
- The Makerule allows a parameter setting to be computed from its parents
- A Makerule is associated to the relation between two parameter types,
  typically they are written per dependent parameter type
- A trim changing a high level parameter can be automatically propagated down
...
GTS1KY1/KL
GTS1MU1_TO_GTS1DI4S/BRHO
CurrentMakeRule
for relation BL→I
GTS1KY1/BL
GTS1KY1/I
GTS1KY1/Setting#current

---
LSA Trim: Makerule 2/2
Example: CurrentMakeRule

---
LSA Trim: Linkrules
- Link rules generate the link between two beam-in beamprocesses
- Generate settings for the part of the pattern without beam
- Physics parameters only exist when there is beam,
  hardware parameters are always there, thus Linkrules are only used for hardware parameters (e.g. current)
LSA Model Overview - LSA TEAM - © CERN 2004

---
LSA Trim: Incorporationrule
- Ensures continuity of functions within the pattern
- Propagates changes from one beam process to its neighbours
- Defined per beamprocess type

---
Agenda
- LSA System, LSA @ GSI
- Concepts in LSA
  - Accelerators and Layout, Parameter Hierarchy
  - Contexts
  - Settings
  - Trim
- LSA API and Examples

---
LSA Setup and Usage
- Set up of LSA:
  - definition of the accelerator, import of devices, import optics
  - model the parameter hierarchy and define propagation rules
- Using LSA:
  - Defining e.g. a new pattern calculating all values,
    the values are then stored in the database
  - Drive new settings to the hardware, execute the new cycle
  - Trim values and send the changed settings to the hardware,
    all trims are stored in the database
  - Monitor device values
  - Supply other systems with necessary information about settings
  - API for applications to get information from the settings management system and to perform trims

---
LSA API Examples 1/3
- Convenience Class Services to retrieve LSA Services, e.g.
  - Services.getAcceleratorService()
- AcceleratorService
  - Set<Accelerator> findAccelerators();
  - Set<TransferLine> findTransferLines();
- DeviceService
  - Set<Device> findDevices(DevicesRequest request);
- ParameterService
  - Set<Parameter> findParameters(ParametersRequest request);
  - Set<ParameterTreeNode> findParameterTrees(
            ParameterTreesRequest request);

---
LSA API Examples 2/3
- ContextService
  - Pattern findPattern(String name);
  - Set<Pattern> findPatterns();
  - Set<Pattern> findResidentPatterns();
  - Set<PatternGroup> findPatternGroups();
- SettingService
  - ContextSettings findContextSettings(StandAloneContext context);
- TrimService
  - TrimResponse trimSettings(TrimRequest request) throws
            TrimException, DriveException;
  - TrimResponse revertTrim(RevertTrimRequest request) throws ..
  - TrimResponse copySettings(CopySettingsRequest copyRequest) throws ..
- And others:
  - OpticService: find optics, twiss, ion optical elements,..

---
Contacts
- LSA Team (ACO APP):
  Raphael Müller Andreas Schaller Hanno Hüther
  (LSA Projektleiter)
- FAIR Datenversorgung / FAIR data supply:
  - David Ondreka (SYS)
- Papers:
  - ICALEPCS 2017: First Production Use of the new Settings Management System for FAIR
  - PCaPAC 2010: Settings Management within the FAIR control system
    based on the CERN LSA Framework

---
LSA API Examples 3/3
=> Hands-on Session :-)