AI4S FESA Interface
Property name	Property / type	Field name	Field type	unit	description
Status	status
		status-item	GSI-status-field		OK/ERROR
		detailed-status-field	GSI-Detailed-status-field		0 – Motor fault / 1 – Communication fault / 2 – Internal fault
		ai4sStatus	bitset	/	0 – X Motor fault / 1 – Y Motor fault / 2 – Over temperature / 3 – Internal communication state / 4 - External communication state / 5 – 24V state / (0=OK ; 1=FAULT)
Power	power				Always ON.
Reset	reset				Reset device
Init	init				?
Version	version				Fesa version, class version, HW version, ?
StubXStop	command	/	/	/	Puts stub X in “stop” mode or out of “stop” mode
StubYStop	command	/	/	/	Puts stub Y in “stop” mode or out of “stop” mode

Setting	setting	positionX	float	/	Stub X position setpoint
		positionY	float	/	Stub Y position setpoint

Acquisition	acquisition	positionX	float	/	X Stub read out
		positionY	float	/	Y Stub read out
		ai4sStatus	bitset	/	0 – Motor fault / 1 – Communication / 2 – Over temperature / 3 – Internal communication state / 4 - External communication state / 5 – 24V state
		setPositionX	float	/	Stub X setpoint
		setPositionY	float	/	Stub Y setpoint
		signalLevelX	int	/	05000 = no signal (matching ok or / no microwave)
		signalLevelY	int	/	05000 = no signal (matching ok or / no microwave)

Configuration	setting	stubXAutoMode	bool	/	True = Automatic mode / False = Manual mode
		stubYAutoMode	bool	/	True = Automatic mode / False = Manual mode