The FESA Development Guideline

---
Overview
Overview
- Why we need a GSI – Convention ?
- Wiki: “development workflow for productive classes”
  - Read + use the “FESA Development Guideline” !!
  - Work together with CSCO/AP
  - Provide a Mock !
  - ...
- “Add Class”  GSIClassTemplate
- GSI-specific-elements will be enforced for productive classes !
- Use the FESA-browser to read the documentation of each xml-element.

---
Properties
Properties

---
Properties - Init

---
Properties - Reset

---
Properties - Setting
- any number of GSI-Setting-Properties
- one has to be named 'Setting'
- Prefix 'Expert' if the property should only be used by equipment-experts

---
Properties - Acquisition
- any number of GSI-Acquisition-Properties
- one has to be named 'Acquisition'
- Prefix 'Expert' if the property should only be used by equipment-experts

---
Properties - Acquisition
Acquisition meta-data -
field suffixes to use:
_status
_min / _max
_toAbs
_ tolRel
_tolCheckMode
_units
Set
AQN_STATUS
NOT_OK
BAD_QUALITY
DIFFERENT_FROM_SETTING
OUT_OF_RANGE
BUSY
TIMEOUT
…

---
Fields (Acquisition-Property)
Properties - Acquisition

---
Properties - Version

---
Exercise I
Download the GSI Development Guideline from the FESA Wiki
→ FESAHome → Development workflow for productive equipment software
Create a new FESA class by using the 'GSIClassTemplate'
Add a device-setting field 'voltage'(double) and provide it in the GSI-Setting-Property
Add fixed 'min-value-item' and 'max-	value-item' for 'voltage' and set the range to [ 0, 100 ]
→ check the Slides / GSI Guideline for proper naming
add child → 'default'. Here you can place a value.
Add a field 'measVoltage'(double) and provide it in the 'GSI-Acquisition-Property'
→ name the value-item in the property 'voltage'
Add a periodic RT-Action (Wizard insert RT-Action) which just copies voltage to measVoltage
Add a field 'measVoltageSet' and provide it in the 'GSI-Acquisition-Property'
→ check the Slides / GSI Guideline for proper naming for this new value-item
In the RT-Action, set 'measVoltageSet' to 'voltage'
for real hardware, 'measVoltageSet' should come from the hardware-device
Add information about the used unit for voltage and voltageSet in all properties
→ check the Slides / GSI Guideline for proper naming and the unit which is to use
Add a new version-item to the GSI-Version-Property
→ Name it 'fakeFirmwareVersion'

---
Properties - Power

---
Fields (Power-Property)
Properties - Power
Enum (1=ON, 2=OFF, 3=STANDBY )
Desired power-state of the device ( not to confuse with DEVICE_POWER_STATE )

---
Properties - ModuleStatus

---
Properties - ModuleStatus
Enum( 0=UNKNOWN, 1=OK, 2=WARNING, 3=ERROR, 4=NOT_AVAILABLE )

---
Properties - Status

---
Fields (Status-Property)
Properties - Status
Enum( 0=UNKNOWN, 1=OK, 2=WARNING, 3=ERROR )

---
Properties - Status
Enum( 0=INFO, 1=OK, 2=WARNING_ON_FALSE, 3=ERROR_ON_FALSE

---
Properties - Status
Enum ( 0=UNKNOWN, 1=ON, 2=OFF, 3=STANDBY, 4=POWER_DOWN, 5=POWER_UP )

---
Properties - Status
Enum ( 0=REMOTE, 1=LOCAL )

---
Properties - Status
Pasted from HTML-Doku:
This GSI specific field is used to signal that the device is ready to be used operationally in the facility.
Usually that implies that the field status signals "OK" or "WARNING", the field control signals "REMOTE" and the field modulesReady signals "true". For most devices the value of "opReady" does not change when the hardware device is turned on/off.
If the usual logic does not apply for a specific device, exceptional logic should be described in the documentation of the related FESA class!

---
Properties - Status
- store last 16 errors for the clients
- logs error to central logging system

---
Properties - DeviceDescription

---
Exercise II
Fill the field 'acquisitionContext' by using the method 'insert'
- Check the FESA-Wiki:
v3.1.0 → C++ CodeSnippets → Working with fields → Fill the GSI-acq-context-field
In the RT-Action, check the value of the field „power“
- Write '0' to 'measVoltage' if the power is 'OFF'
Fill all fields of the GSI-Status-Property in the RTAction
- status → OK
- detaileStatus
→ set true to both items ( names can be found in configuration → detailedStatus_labels )
→ check the C++ CodeSnippets in the Wiki ! ( Usage of the GSI-detailed-status-field )
- powerState → same as setting value 'power'
- control → remote
- interlock → false
- opReady → true
- modulesReady → true
Fill the field 'moduleStatus' of the GSI-ModuleStatus-Property in the RTAction
- ( names can be found in configuration → moduleStatus_labels )
- check the C++ CodeSnippets in the Wiki ! ( Usage of the GSI-module-status-field )
Report an fake-error to the field 'error_collection' in the RTAction
- check the C++ CodeSnippets in the Wiki ! ( Report an error by using the GSI-error_collection-field )

---
Misc – Doc Creation

---
Misc – Doc Creation
„upload doc. to webserver“
Better dont press this one ( at your own risk, it killed my eclipse! )

---
Misc – Conditions
„Handle GSI Condition“

---
Misc – Mocking

---
Exercise III
Add documentation to the value items and field you added
Usually there is no need to document the meta-fields
Press the 'create doc' items in order to generate html-documentation for the class
Press 'Handle GSI Condition' and add an Exeption Message and an error-code
Add a device-specific boolean configuration field 'isMockDevice'
In the RT-Action, always set the measured voltage to 99 for the mock-device
build up the DeployUnit, add a FEC
Fill the instantiation file with one device until it is valid ( use 1000ms for timer event )
Press 'Create Mock instance' to get a second instance-file

---
Thanks for your attention!
Thanks for your attention!