Event Sources
and
Realtime Actions

---
Actions
Fesa maintains strict separation of Server and Realtime parts
Fesa maintains strict separation of Server and Realtime parts
- Server Actions:
  - Manage the client interface
  - May only read acquisition data
  - Triggered by middleware requests
- Realtime Actions
  - Manage the hardware interface
  - May write acquisition data
  - Triggered by Events
  - Events generated by Event Sources
The Server and Realtime parts may run in separate executables
The Realtime hardware interface can keep running if the middleware interface crashes

---
Data Consistency
A data consistency mechanism ensures there is no conflict if a single data field is simultaneously read by a Server Action and written by a Realtime Action
RollingBuffer size 2:
Time	RT Action	Server GetAcquisition Action
0	Hardware value into Buffer 0
1	Hardware value into Buffer 1	Read Buffer 0
2	Blocks	Still Reading Buffer 0
3	Hardware value into Buffer 0

---
Event Sources
Source Cardinality Class specific Payload possible
TimingEventSource	(0..1)	no	yes
TimerEventSource	(0..1)	no	no
CustomEventSource	(0..n)	yes	yes
OnDemandEventSource	(0..n)	yes	yes
OnSubscriptionEventSource	(0..1)	no	yes
Generated FESA class code
Event (Server)
Get
Set
Subscribe
Unsubscribe
Event (RealTime)
Timer
Timing (White Rabbit)
Custom (Hardware)
OnDemand (internal)
OnSubscription
Server Interface
RT Scheduler
C++ Code
provided by the class developer
Hardware Device
Hardware Device
Hardware Device

---
Event Source Types
- TimingEventSource
  - Events defined by LSA and distributed by the White Rabbit timing system
- TimerEventSource
  - Generates events at regular intervals, typically used to poll hardware
- CustomEventSource
  - Allows hardware to trigger a Realtime Action
- OnDemandEventSource
  - Allows a client to trigger a Realtime Action from a Server Action
- OnSubscriptionEventSource
  - FESA classes may subscribe to other classes' Properties

---
Timing Event Source
Timing Master distributes events and their scheduled execution time
Timing Receivers match the events you are interested in
Events are triggered at the scheduled time
May have as many timing-events as the hardware supports
Covered in detail in the next section

---
Timer Event Source
Provides a software interval timers with configurable period (ms)
Multiple timer events may be used
Typically used to poll hardware for acquisition data
Always present in class-design
no payload

---
Event Lifetime
Example: Timer Event
  - TimerEventSource waits until a certain time is reached
  - TimerEventSource generates an Event of a particular LogicalEvent type
    The Logical Event is e.g. ReadTemperature
    The Event is a single object and may carry a payload
  - A Scheduling Unit assigned to that LogicalEvent type defines which Action(s) the Event will trigger
  - The Event is queued and processed according to Scheduling Unit and Concurrency Layer rules
  - An Action is triggered, allowing user code to act on the Event and any payload

---
Design Steps
- Design
  - Event Source
  - Logical Events
  - Actions
  - Scheduling Units
- Deploy Unit
  - Concurrency Layers: Assign Scheduling Units Threads and Processor Affinity
- Instance File
  - Event Mapping: Linking Event Sources to Logical Events

---
Custom Event Source
You may create your own event-source
Typically used when the hardware drives the acquisition process
Your code determines when an event is triggered
Interrupts
Callbacks
Polling
You may produce many custom-events in a custom-event-source

---
A Custom Timer
The default behaviour is to block for a short time interval
This gives an alternative way to build a Timer Event Source
Design:
Create a new FESA Class named EventSources
and create the default deploy-unit

---
Custom Event Design
Create a new real-time action using the
RT Action Wizard
Add a custom-event-source at events→sources
The relevant sections of the design should be
as shown

---
Custom Event Code
After generating code you will have new files CustomTimerAction.cpp and CustomTimerEventSource.cpp
Modify the Action to do something visible
void CustomTimerAction::execute(fesa::RTEvent* pEvt)
{
std::cout << "Custom Timer Event" << std::endl;
}
void CustomTimerEventSource::wait(boost::shared_ptr<fesa::RTEvent>& eventToFire)
{
// This code provides an example on how a custom-event-source can look like.
struct timespec time;
time.tv_sec = 1;	// wake-up every 1 second
time.tv_nsec = 0;
// Your code should block until something interesting happens
nanosleep(&time, &time);
// Here you can create your own event by filling the eventToFire with the needed information.
// Use the Event-Enumeration defined in the header file of this class!
// Check the BaseClass of this class for more options!
createEvent(eventToFire, CustomTimerEventSource::defaultEvent);
// Once this method returns, the fesa-core will process our event and post it to all interested schedulers.
// After that, this method will be called again.
}

---
Custom Event Configuration
In the Deploy Unit:
Add a scheduler
Name the concurrency layer
Add a scheduling unit and reference the one in the design
Remove executable type server and replace with mixed
Generate Code
Add FEC (asl...)
In the Instance File add an event configuration
Under Custom Add CustomTimerEventSource
(keep the defaultEvent)
Use “Promote Instances” if events added to the
design are not present in the instance file

---
Custom Event Execution
Cd yourworkspace/EventSources_DU/src/test/asl73x
./startManually_EventSources_DU_M.sh
Watch the events
Use Promote Instances if events added to the
design are not present in the instance file

---
OnDemandEventSource
ServerAction triggers RTAction
RTAction triggers RTAction
any number of class-specific instances
manual or automatic trigger
payload
TriggerOnDemandEventSource( MyOnDemandEventSource, context );
std::string payload = "myPayload";
TriggerOnDemandEventSource( MyOnDemandEventSource,context,payload.c_str(),payload.size() );

---
On Demand Event Source
Goal: Allow a client to initiate a real-time action
Using the Property Wizard create a command-property “Demand”
Select default implementation for the SetDemandAction
Create an on-demand-event-source DemandEventSource
Start the RT Action Wizard to create:
a Logical Event StartDemandEvent of type on-demand
An Action StartDemandAction
A Scheduling Unit
Add a triggered-event-source to the SetDemand
action referring to the On-demand event source
DemandStartMeasurement

---
On Demand Event Source
Goal: Initiate a real-time action
Deploy:
Mixed Executable
Create a concurrency layer
Add the scheduling unit
Instance:
Name the event-configuration measureOnDemand
Name the Device
In the device events-mapping, set the event-configuration-ref
Start FESA Explorer and trigger the command property
The Set action returns immediately
The realtime action is triggered

---
Payloads
Events carry a payload of type string.
Realtime actions can check if an event carries a payload
TriggerOnDemandEventSource( DemandEventSource, context );
std::string payload = "myPayload";
TriggerOnDemandEventSource( DemandEventSource,context,payload.c_str(),payload.size() );

---
Further Exercises
Create acquisition data fields and a property to access them
Use a payload to transfer data from server to RT

---
Event Payloads
Use of Event Payloads
Deploy:
Mixed Executable
Create a concurrency layer
Add the scheduling unit
Instance:
Name the event-configuration measureOnDemand
Name the Device
In the device events-mapping, set the event-configuration-ref
Start FESA Explorer and trigger the command property
The Set action returns immediately
The realtime action is triggered
It could notify via subscription when completed

---
Enabling and Disabling Event Sources
name of the logical-event
service-locator of class Ex04
deprecated argument, can be ignored
name of the event-source

---
OnSubscription Event Source
→ move to class reltionships
FESA classes may subscribe to properties of other classes using the same
middleware mechanism applications use
An Event is triggered whenever the remote class notifies that there is new data
The Event contains the data in its payload