RealTime and Timing
Real-Time behaviour and Timing
[Speaker Notes: CERN BE/CO FESA: Introduction]

---
What is a Real Time System?
What is a Real Time System?
  - A system is said to be “real-time” if the correctness of an operation depends not only upon its logical correctness, but also upon the time in which it is performed. Real-time systems are classified by the consequence of missing a deadline.
  - Hard real-time: Missing a deadline is a total system failure.
    - Use hardware such as an FPGA triggered by the timing system.
    - Use FESA to configure the hardware
  - Soft real-time: The usefulness of a result degrades after its deadline, thereby degrading the system's quality of service.
    - Use FESA software triggered by the timing system
  - No real-time requirements:
    - Use FESA software triggered by the conventional network
[Speaker Notes: CERN BE/CO FESA: Introduction]

---
Performance – FESA + RT-Linux
Performance
FESA + Linux
Time between receiving hardware-trigger and execution of a RT-Action
55h
10M measurements
1MB/sec network load
10MB/sec filesystem load
used FESA v. 3.0-beta
early version of the SCU

---
Timing System
Devices that require accurate timing are connected to both the White Rabbit
Timing Network and the middleware Ethernet network
A Data Master distributes Timing Events and execution times
Timing Receivers trigger hardware and software
Slow Devices can be accessed over middleware with no performance guarantees

---
Timing Messages
Message Format
EventID
GroupID – The timing group where the FEC is located
Event Number – The event your software is interested in
Sequence - Multiplexing
Process - Multiplexing
Parameter
Beam Production Chain – Involves many timing groups and FECs
Beam Production Chain Start Time

---
Timing Groups
The CRYRING Project is a
testbed for the new
FAIR White Rabbit
timing system
C
Timing Group
200	0xC8	YRS1	CRYRING source 1
201	0xC9	YRLE	CRYRING low energy linac
202	0xCA	YRME	CRYRING mid energy linac
203	0xCB	TYR1	Transfer into CRYRING
210	0xD2	CRYRING_RING	CRYRING ring
211	0xD3	CRYRING_COOLER	CRYRING electron cooler

---
White Rabbit Timing Events
The sequence of operations required to produce a beam is determined by LSA
LSA transfers Timing Events to the Timing Data Master
The Data Master transmits Events and their execution time to the Timing Receivers
FESA software can be triggered by these events
256	0x100	CMD_BP_START	Start of Beam Process
257	0x101	CMD_SEQ_START	Sequence start.
270	0x10E	CMD_SOURCE_BEAM_ON	Source Beam On
271	0x10F	CMD_SOURCE_BEAM_OFF	Source Beam Off
272	0x110	CMD_SOURCE_HV_PREP	HV Preparation for the Source
280	0x118	CMD_BI_TRIGGER	Beam Diagnostics: Trigger
281	0x119	CMD_BI_MEAS1	Beam Diagnostics: Measure Event 1
282	0x11A	CMD_BI_MEAS2	Beam Diagnostics: Measure Event 2
290	0x122	CMD_RF_PREP	RF: Prepare device for pulse generation
291	0x123	CMD_RF_PREP_PAUSE	RF: Prepare device for pulse generation
292	0x124	CMD_RF_STOP_PAUSE	RF: Stop generation of pulse
518	0x206	CMD_BEAM_ON	General: Begin of beam passage
520	0x208	CMD_BEAM_OFF	General: End of beam passage

---
ECA and SAFTlib
Event-Conditon-Action processor
Conditions specify the Timing Group and Event of Interest
Matches trigger software and hardware actions
SAFTlib
Software interface to the ECA of the Timing Receiver
Allows multiple software processes to register for timing events
Allows software to register Hardware events – e.g.triggering the SCU bus
in response to a timing event
FESA uses SAFTlib to drive the Timing Event Source
SAFTlib can be simultaneously used via FESA and directly
May have as many timing-events as the hardware supports

---
Exercise: Timing Events
This exercise will build a class that illustrates the timing system interface
- Design a class with a Timing Event Source
- Trigger a Real-time action
- (Optional) Do something useful
- Deploy onto an SCU with a White Rabbit timing connection

---
SCU
To test FESA software and Timing we need a Frontend computer connected to
the White Rabbit network
We will be using scuxl0019
Connect: ssh root@scuxl0019
password: fesakurs
To view timing events use the saft-ctl utility's snoop function:
saft-ctl yourpcnumber snoop 0 0
Time: 2016-04-22 08:54:09.651841592 ID: 0x00ca124003000c00 Param: 0x0000000000000000
Time: 2016-04-22 08:54:09.652841592 ID: 0x00ca122003000c00 Param: 0x0000000000000000

---
Voltmeter Design
Everyone will be releasing to the same SCU
Make your Class name unique to avoid conflicts
Recommend name VoltmeterNN when NN=your PC number
Create a new Class and Deploy Unit
VoltmeterNN
VoltmeterNN_DU
Create a Realtime Action using the RT-Wizard
Logical Event: MeasurementEvent
Type: timing
RTAction: MesureVoltageAction
SU: MeasureVoltageSU
Generate Code
Add some output or logging code to MeasureVoltage.cpp
void MeasureVoltage::execute(fesa::RTEvent* pEvt)
{
std::cout << "Measuring Voltage" << std::endl;
usleep(200000);
std::cout << "Finished Measuring Voltage" << std::endl;
}

---
Scheduling Units and Concurrency
Scheduling Units are defined in the Design and link Events to Actions
For actions that take significant time to execute you may adjust the scheduling
behaviour in the Deployment Unit under the scheduler element
The scheduler can have a number of concurrency layers
A layer can contain multiple scheduling-units
A layer by default operates in a single thread
A layer has a priority relative to other layers
Multithreaded per-device
The Threading-policy of a scheduling-unit may be changed to per-device-group
to parallelize a single action on multiple devices
Multithreaded per-action
Place scheduling-units in separate concurrency layers

---
Priorities
Priorities depend on the runtime environment
Realtime Scheduling
Linux RT Priorities (1 low to 99 high)
Used on SCU
Non Realtime Scheduling
Linux Nice Priorities (19 low to 0 high (negative with root permissions)
Used on ASL development machines
Selected with –noRTSched flag
Set in Instance File
Prio-management element
Can set priority for each concurrency layer

---
Voltmeter Deployment
In your Deploy Unit
Change executable from Server to Mixed
Add a scheduler
Name the concurrency layer
Link the scheduling-unit to your design
Generate Instance File
Select Deploy Unit
Create FEC scuxl0019
with FAIR Timing

---
Instance File
Timing Configuration for the Device
Name your Device
Set timingDomain to FAIR
Set accelerator to CRYRING
Set acceleratorZone to YRLE#201
Events Mapping for the Class
Create an event-configuration for MeasurementEvent
Name it SeqStart
Under Timing Configuration – hardware-event the
available timing events are in a drop-down menu
Set the hardware-event to CMD_SEQ_START#257
Events Mapping for the Device
Set the configuration reference for
MeasurementEvent to the Timing
Configuration you created above

---
SCU Software Deployment
The deployment process copies software to an NFS-exported directory
On ASL:
/common/export/fesa/local/scuxl0019
As your software is still in development
The deployment directory will be:
/common/export/fesa/local/scuxl0019/VoltmeterNN_DU-d
For SCU development testing, this is mounted read-only at the path:
/opt/fesa/nfs/local/scuxl0019/VoltMeterNN_DU-d
Start with
./startManually_VoltmeterNN_DU_M.sh
FESA classes deployed for production are started automatically
during the boot process

---
Further Development
The class as-is will be built on in the Multiplexing session
Suggestions for exploration:
Add Data fields and Acquisition Properties
Register for multiple events (please limit to 256)
Place scheduling units in separate concurrency layers for multithreading
Adjust the priority of concurrency layers
Processor affinity
Event Queue size
Event Queue behaviour – test a fast source and slow action
Link a single event to multiple actions using multiple scheduling units

---
Further Development

---
Event Mapping
Event Mapping
Add any number of event-configurations per logical event.
[Speaker Notes: CERN BE/CO FESA: Introduction]

---
Event Mapping
Choose different event-configurations per device.
[Speaker Notes: CERN BE/CO FESA: Introduction]