## Slide 1: Data consistency & data store
FESA Advanced

## Slide 2: Agenda
Problems with previous framework
More problems with the new CPUs
FESA 3 solutions
Fields types
Field type decision trees

## Slide 3: Typical priorities
we typically give a lower prio to the server threads
E.g. RT around 50 and server around 25
Sometimes, we give even lower prio for some properties (FESA 2.10 background props)

## Slide 4: Settings problem
Datastore
Server writes
new settings
RT writes
settings in HW
The RT uses inconsistent settings
Inconsistent
Datastore
Server writes
new settings
RT writes
settings in HW
Inconsistent
The RT uses consistent settings


set
set

## Slide 5: Acquisition problem
Datastore
Server updates
clients
RT writes
acquisition
Datastore
Server updates
clients
RT writes
acquisition
The server sends consistent data

The server sends inconsistent data

Inconsistent

## Slide 6: Agenda
Problems with previous framework
More problems with the new CPUs
FESA 3 solutions
Fields types
Field type decision trees

## Slide 7: New CPU New problems
Intel Core 2 DUO L7400 – 2 cores w/o hyperthreading
2 cores  2 threads run in parallel whatever the prio
Datastore
Server writes
new settings
RT writes
settings in HW
Inconsistent
The RT uses inconsistent settings

Inconsistent
Similar problem for the acquisition case
Playing with prio no longer helps with data races
set

## Slide 8: Agenda
Problems with previous framework
More problems with the new CPUs
FESA 3 solutions
Fields types
Field type decision trees

## Slide 9: FESA 3 solutions Settings
Settings flow as defined in FESA 3 is
High-level  Server part  RT part  Hardware
Double-buffer mechanism to protect against data races
Datastore
Server writes
new settings
RT writes
settings in HW
set
Inconsistent
OK
RT sync
OK
The RT uses consistent settings

RT sync done in the RT part
Very cheap pointer swapping  very little jitter introduced
pending buffer (server)
active buffer (RT)

## Slide 10: FESA 3 solutions Acquisition
Acquisition flow as defined in FESA 3 is
Hardware  RT part  Server part  High-level
Rolling-buffer mechanism to protect against data races
Uses the cycle-stamp to select the buffer
Implementation hidden  you don’t have access to the other buffers
Datastore
Updates for X
Server updates
clients
RT writes
acquisition
Data for cystamp X
Cystamp Y
Z
Discards
data
for X
The clients receive consistent acquisitions


## Slide 11: Agenda
Problems with previous framework
More problems with the new CPUs
FESA 3 solutions
Fields types
Field type decision trees

## Slide 12: Field types
There are 5 types of fields
  Configuration
  Setting
  Unshared setting
  Acquisition
  Generic
Configuration field
  Read-only from anywhere
  Default field in the configuration section

## Slide 13: Field types
Setting field
  Shared and data-consistent (double-buffer)
  Read-write from server
  Read-only from RT
  Default field in the setting section
  Buffer swap by RT part
Unshared setting field
  Not visible from RT
  Setting field’s attribute “shared” = false

## Slide 14: Field types
Acquisition field
  Shared and data-consistent (rolling-buffer)
  Read-only from server
  Read-write from RT
  Default field in the acquisition section
  Works with the cycle-stamp in the context
Generic field
  Accessible from anywhere and without any protection
  Any field’s attribute “data-consistent” = false
  Should be used for private fields only

## Slide 15: An example
6 fields – all int32_t
1 configuration field – configField
3 setting fields
  serverField – a server only field (i.e. not shared)
  sharedField – a double-buffer field
  unprotectedField – a generic field w/o protection
2 acquisition fields
  rollingField – a rolling-buffer field
  rtField – a generic field w/o protection (RT use only)

## Slide 16: An example Design

## Slide 17: An example device.h
class Device : public fesa::AbstractDevice
{
public:
Device();
ConfigFieldScalar<int32_t> configField;
SettingFieldScalar<int32_t> serverField;
SettingFieldScalar<int32_t> sharedField;
GenericFieldScalar<int32_t> unprotectedField;
AcqFieldScalar<int32_t> rollingField;
GenericFieldScalar<int32_t> rtField;
};

## Slide 18: An example Device constructor
Device::Device() :
configField("configField",this),
serverField("serverField",true, false, this, true, false),
sharedField("sharedField",true, false, this, true, true),
unprotectedField("unprotectedField",true, this, true),
rollingField("rollingField",true, this, false),
rtField("rtField",true, this, false)
{
}
Note: double-buffer fields and unshared fields have same impl. Only the last arg is different

## Slide 19: Rolling buffer depth configuration
Rolling buffer’s size in the instantiation file
Minimum 3 slots
Maximum deps on the FEC memory

## Slide 20: Agenda
Problems with previous framework
More problems with the new CPUs
FESA 3 solutions
Fields types
Field type decision trees

## Slide 21: Which setting field?
Do I need to access the field from the RT part?
Setting field with @shared=false
Do I need to write into the field from the RT part?
Is the field private to the RT part?
Setting field with @data-consistent=false
Setting field with @data-consistent=false
Setting field with default values
N
Y
N
Y
N
Y
You must provide your own data protection mechanism
ǃ

## Slide 22: Which acquisition field?
Is the field private to the RT part?
Acquisition field with @data-consistent=false
Do I need to keep the value from the previous execution?
Acquisition field with default values
2 separate fields:
1 private & 1 w/o history
Y
N
Y
N
start over for each field