Data-Types

---
- With FESA3 we distinguish between default types and custom types (user defined types)
  - default
    - scalar
    - array
    - array2D
  - custom
    - custom-type-scalar
    - custom-type-array
    - custom-type-array2D

---
Scalar data types
- + custom types
- type “char” currently only for arrays

---
Array(2D) data types
- Use the context menu (rightclick on item)
- arrays can have different dimensions
  - one-dimensional (i.e. “string”)
  - two-dimensional (i.e. “string-array”)
  - a dimension can be constant or device-specific (variable)
- arrays can contain custom types

---
Custom data types
- Custom-types can be used in the design and in the C++ code
- Like in plain code, they make things more readable, prevent duplication and stop the usage of “magic-numbers”
- Use them whenever possible!

---
Custom data types
- enum
  - name to use in design and C++ code
  - items
    - Unique value
    - symbol to use in code
    - access (RW, RO, WO)
- state-enum
  - More or leass the same than enum
  - Some values predefined
- constant
- struct
- bit-enum 16bits
- bit-enum 32bits

---
Custom data types
- enum
- state-enum
- constant
  - type can be any scalar-type
  - define the value in the design
- struct
- bit-enum 16bits
- bit-enum 32bits

---
Custom data types
- enum
- state-enum
- constant
- struct
  - struct-item type can be any fesa-data-type
  - currently not possible to send structs directly via the middleware
- bit-enum 16bits
- bit-enum 32bits

---
Custom data types
- enum
- state-enum
- constant
- struct
- bit-enum 16bits
  - Can be used as bitmask to address single-bit in the C++ code
  - only for scalar-types
  - often used for hardware-components
  - will get further updates in coming fesa-versions
- bit-enum 32bits
  - same as bit-enum 16bits, just more bits

---
Mission
- Create a class which periodically measures an array of values(use random values) in the RT-Action.
- The measured array has to be offered by an acquisition-property.
- Use a custom-type for the array-size.
- Use custom-types to define the minimum and maximum rand-values.
- The client should be able to switch the measurement ON and OFF. Use an enum-type for this.
  (Manual Notification!)
On any problems: fesa-support@gsi.de

---
Thank you for your listening !!