microIOC - HW specific settings

microIOC with RS232 and GPIB interface

Table of Contents

1. Configuration	3

2. microIOCs configuration	4

2.1. microIOC serial number: 091207-A2-A3090100-000-00214	4

2.1.1. PC/104 card: SERIAL CARD	4

2.1.2. PC/104 card: GPIB CARD	4

3. Description of connections	5

3.1. Back-panel connections	5

3.1.1. RS232 communication ports	5

3.1.2. GPIB port	6

4. Product Information	7

# Configuration

|  | microIOC serial number: 091207-A2-A3090100-000-00214 |
| --- | --- |

This microIOC is customized to provide serial RS232 and GPIB functionality.

|  | The purpose of this document is to provide configuration and settings, specific to the microIOC, having the before-mentioned serial number. For detailed explanation and usage please refer to microIOC HW installation and users manual. |
| --- | --- |

# microIOCs configuration

## microIOC serial number: 091207-A2-A3090100-000-00214

### PC/104 card: SERIAL CARD

| serial number: | TV07513316 |
| --- | --- |
| card type: | PM1028-8-R20 |

#### JUMPER SETTINGS FOR SERIAL CARD

| Configuration of PC/104 card: PM-1004 | Configured values |
| --- | --- |
| Base Address Setting: | 200H |
| Status Address Setting: | 320H |
| IRQ: | 9 |
| Serial mode selection | RS232 |

Table 1: Jumper settings configuration for PC/104 serial card

### PC/104 card: GPIB CARD

| serial number: | 29554 |
| --- | --- |
| card type: | PC104-GPIB |

#### JUMPER SETTINGS FOR GPIB CARD

| Configuration of PC/104 card: GPIB | Configured values |
| --- | --- |
| Base Address Setting: | 300H |
| IRQ: | 5 |

Table 2: Jumper settings configuration for PC/104 GPIB card

# Description of connections

On the back panel of microIOC can be found different types of ports:

- 8 X RS232 serial port (DB9M connector; ttyS4,ttyS5,ttyS6,ttyS7, ttyS8, ttys9, ttyS10, ttyS11)

- 1 X GPIB port (GPIB connector)

## Back-panel connections

### RS232 communication ports

| Serial communication port nr. | SW name for communication port |
| --- | --- |
| SER1 – ttyS4 | /dev/ttyS4 |
| SER2 – ttyS5 | /dev/ttyS5 |
| SER3 – ttyS6 | /dev/ttyS6 |
| SER4 – ttyS7 | /dev/ttyS7 |
| SER5 – ttyS8 | /dev/ttyS8 |
| SER6 – ttyS9 | /dev/ttyS9 |
| SER7 – ttyS10 | /dev/ttyS10 |
| SER8 – ttyS11 | /dev/ttyS11 |

Table 3: Description of serial communication ports

Figure 1:  Back panel serial port description

### GPIB port

For controlling of GPIB devices GPIB port is used on back panel. The position of GPIB port can be seen on picture below.

Figure 2: back panel GPIB port description

# Product Information

For additional specifications, upgrades, and customer-specific customizations please contact:

|  | Sales and Customer Support Tel: +386 1 477 66 76 Fax: +386 1 477 66 10 E-mail: info@cosylab.com E-mail: microioc@cosylab.com |
| --- | --- |

Complete information about other products and services of the Cosylab Company is available on the following web-pages:

|  | www.cosylab.com www.microIOC.com |
| --- | --- |

At Services & support you can check Frequently Asked Questions about microIOC:

|  | www.microioc.com/services_and_support |
| --- | --- |

We are aware of the possibility of ambiguities or errors in this manual. Any feedback pointing out those places would be highly appreciated. Please use the upper contact information.